## Slide 1
A Prudent Framework for Understanding Risk-Awareness in Demand Response
-------Group meeting
Original title: Prudent Price-Responsive Demands
Liudong Chen
Earth and Environmental Engineering
Columbia University
Jun. 25. 2025

## Slide 2
Prudent Price-Responsive Demands
Price-Responsive
2|
Prudent
Time
Demand
Time
Uncertainty
If uncertain events happen, prudent decision-makers will do sth. to respond to the event
Time-dependent system:
Decision makers do sth. ahead of time
Economic: seeing ahead, sagacity
Demands

## Slide 3
Toy example:
Suppose you have a battery and participate in the real-time market with price uncertainty.
You need to decide on charge or discharge starting now until the price is realized
3|
What will you do?
Now, I told you future price variance increase, but the expectation is the same.
Price pdf
Future price
Time

## Slide 4
Background
Problem formulation
Main Results
Case Study and Conclusion
4|

## Slide 5
Background
Motivation
5| Background
Consumers become more responsive
United States DER integration increase
https://en.wikipedia.org/wiki/Solar_power_in_the_United_States
https://www.eia.gov/todayinenergy/detail.php?id=60341
https://www.woodmac.com/news/opinion/transformation-distributed-energy-resource-market/
179 GW solar capacity until 2023
22% are distributed
Consumers installed more smart home devices
https://www.statista.com/statistics/1075749/united-states-installed-base-of-smart-home-systems/#statisticContainer
https://www.techtarget.com/iotagenda/definition/smart-home-or-building
40GW
2.8 Billion
Notes: Small scale – aks distributed solar
EIA - US energy information administration
Smart TV, smart lighting, easy to control and align with user preference, more flexible,

## Slide 6
Background
Dynamic prices incentivize consumers’ responsiveness – uncertainty
6| Background
Understand complex risk-aware behaviors facing (price) uncertainty
Utility companies adopt dynamic tariffs to incentivize demand responses.
https://en.wikipedia.org/wiki/Solar_power_in_the_United_States
https://www.eia.gov/todayinenergy/detail.php?id=60341
https://www.woodmac.com/news/opinion/transformation-distributed-energy-resource-market/
Wholesale markets are inherently uncertain.
Ameren Power Smart Pricing in Illinois
Retail consumer bear huge uncertainty
https://www.coned.com/en/accounts-billing/your-bill/time-of-use
https://www.srpnet.com/price-plans/residential-electric/time-of-use
https://www.oge.com/wps/portal/ord/residential/pricing-options/smart-hours
https://www.ameren.com/illinois/account/customer-service/bill/power-smart-pricing/
Wholesale consumers bear huge uncertainty

## Slide 7
Background
Literature
7| Background
Consumers naturally have high-dimensional and non-linear behavior
Highlight the need for a more sophisticated utility function formulation
https://www.javatpoint.com/group-discussion
Infrastructure
Privacy
Model-driven: Adopt decision-making models with utility functions to represent consumers’ decision-making process
Less data-driven previous works
Face limited application problem
Quadratic
Piecewise linear
Conditional value at risk (CVaR) or robust
Lack of first-principle understanding of risk-aversion motivations
Data-driven
Notes: So, how literature do?
Generally, if you want to know human behavior, behavior economic people will design experiments and collect data, then do some data analysis and combine with statistical tools to reveal the general behavior.
But, due to the infrastructure constraints and concerns about privacy and affordability, it is very difficult to conduct controlled real-world experiments. At least right now, only very few utility company start using smart pricing scheme, such as Ameille mention before, but all the data are private.
So, Consumers’ responses to uncertain prices are less understood in literature. Thus, we need model based formulation.
For example, thermal comfort does not decrease linearly with temperature adjustments or change in a purely quadratic manner. it is influenced
by individual, high-dimensional, non-linear preferences. Also, batteries and many home devices need to operate within strict capacity and ramp rate limits

## Slide 8
Background
8| Background
What do we do
Other practical distribution – mean, variance, skewness, etc. - shape
https://en.wikipedia.org/wiki/Skewness
How does the future uncertainty distribution affect the risk-neutral decision-making process?
Risk operator
Expectation
+ Risk term
https://en.wikipedia.org/wiki/Normal_distribution
Normal distribution – mean, variance
Intentionally
future

## Slide 9
Background
9| Background
Contribution
We establish a theoretical framework to model demand behavior to future volatile electricity prices We model demand with a risk-neutral cost-saving objective in a sequential decision-making context;
Price
pdf
Same expectation
We found that demand models with quadratic cost functions are distribution-insensitive;
We prove that super-quadratic cost functions (higher order than two) result in prudent demands;
We use a simulation with a real-world case to verify our results.
English: Current demand pattern affected by future uncertainty distribution
Math-wise: third-order derivative of the utility function
prudent demands
Notes: CVAR it is prudent, but it is add intentionally, so the model called risk-averse model, but our model here is risk-netural, but is reflect risk-averse behavior.

## Slide 10
Background
Problem formulation
Main Results
Case Study and Conclusion
10|

## Slide 11
Problem Formulation
Demand model
11| Problem Formulation
Discrete time-varying system
X – state (battery SOC)
Stochastic dynamic programming reformulation
P – power consumption (battery charging/discharging)
*Cost function modeling soft and hard constraints
λ – uncertain price
Energy cost
Action cost
State cost
End value function: for value continuity, set to 0
Working backward and recursively solving a single-stage optimization for all time t
Value function: rewards from the future about the current decision, it is a function of time-dependent state value.
Soft
Hard
Linear system transition
Risk-neutral, cost-saving objective

## Slide 12
Problem Formulation
12| Problem Formulation
Definition - Normalized power and state cost
The system is in equilibrium at zero power and state;
Deviate from reference (0) increase discomfort (cost);
Highlight our focus on disturbances and variations.
HVAC system (air conditioning)
Temperature
Set point 25
x = 0
No discomfort
x = -5
Discomfort reflected by cost function C(5)
20
29
x = 4
Discomfort reflected by cost function C(4)
Definition/assumption
Convex and continuous

## Slide 13
Background
Problem formulation
Main Results
Case Study and Conclusion
13|

## Slide 14
Main Results
Theorem 1 – Distribution-insensitive demand models
14| Main results
Quadratic function:
Price
Price distribution set L
Demand model:
Quadratic State cost
Quadratic action cost
Set end value function to 0
Same expectation
Theorem - The demand model at time t-1 is
distribution-insensitive to price distribution at time t
Value function with different uncertainty distribution
Time
t+1
t
Demand model
Demand model
Price distribution
Time domain

## Slide 15
Main Results
15| Main results
Sketch of the proof:
Show the price uncertainty doesn’t affect the value function
Capital letter: function
Lowercase letter: function derivative
Demand model
Demand model
Price distribution
Future price
State cost
Action
Stage cost
Value function
?
Lemma 12
State-related cost
X
Lemma 13
KKT conditions/optimality condition
Lemma 14
First-order derivative
Transformation
Model definition

## Slide 16
Main Results
16| Main results
Corollary – time extrapolation
Demand with quadratic cost function is independent of the future price distribution but only the expectation;
Key takeaway
Demand change
Reference level
Price uncertainty
Price
Price distribution
Theorem - The demand model at time t-1 is
distribution-insensitive to price distribution at time t
Time
t
t-1
Demand model
Distribution insensitive to all future time
T
Same expectation
Time
Widely used quadratic models fail to capture real risk-aware decision behaviors, as they inherently ignore distributional effects and may thus lead to unintended demand pattern changes

## Slide 17
Main Results
17| Main results
Corollary – distribution sensitive demand
Takeaway – problem
Practical situations challenges distribution-insensitive conditions:
Devices show higher-order cost function performance (thermal comfort and hard constraints)
Demand change
Reference level
Price uncertainty
???
Motivated super quadratic formulation – prudent demand
Quadratic function:
Demand model:
Super quadratic function:
Practical price distribution – not symmetrical with zero-mean
Time
Price
Price distribution
Same expectation

## Slide 18
Main Results
Theorem 2 – Prudent demand models
18| Main results
Price
Price distribution set L
Demand model:
Super Quadratic State cost
Quadratic action cost
Set to 0
Same expectation
Theorem - The demand model before time t satisfies prudent and its sensitivity condition to price distribution at time t+1
Value function with different uncertainty distribution
Time
t+1
t
Demand model
Quadratic State cost
Price
Probability
1
Uncertainty
Demand model
Price distribution
Time domain
Sensitivity
Prudent demand
Sensitivity - More skewness
Time
Uncertainty
v(x)

## Slide 19
Main Results
19| Main results
Sketch of the proof:
Show the price uncertainty doesn’t affect the value function
Demand model
Demand model
Price distribution
Future price
State
Value function
Action
?
Lemma 17
State-related cost
Lemma 15
Lemma 16
More skewed
Lemma 18
Probability
Price
KKT conditions/optimality condition
Connect
Showing then
Function property
More skewed uncertainty

## Slide 20
Main Results
20| Main results
Corollary – Distribution & sensitivity extrapolation
Corollary – Strict condition
Prudent theorem
Price
Probability
Expectation
Demand model
Strict condition
Price
Expectation

## Slide 21
Main Results
21| Main results
Our results align with the prudence definition from economics
Key takeaway
Prudent demand’s value function increases with the future price distributional factors, with the same expectation;
Demand change
Prudent demand – Change ahead of time
Uncertainty
The demand level change due to prudence scales proportionally with the skewness of the price distribution, showing the skewness aversion behavior
Sensitivity - The aversion degree increases with skewness
Reference level
Outlier: Symmetrical distribution with the expectation of zero;
Reference level
Skewness aversion
This preparatory behavior reflects an inherent risk-averse response in the demand model; we suggest that the commonly used risk-averse formulations are approximations of a more realistic, higher-order structure.
Notes: Demand level strictly changes ahead of time to respond to risk;
Show skewness aversion

## Slide 22
Background
Problem formulation
Main Results
Case Study and Conclusion
22|

## Slide 23
Case Study
23| Case Study
An illustration example
Quadratic action cost function:
Basic setting
Log barrier state cost function:
Parameter:
2-stage, 2-point price distribution with 0 expectation
Symmetrical uncertainty with 0 expectation and 0 initial state
Price
Probability
0 expectation

## Slide 24
Case Study
24| Case Study
24 stages
The event happens at the 10th stage
6 skewed price distributions with the same expectation and different variance (skewness)
Continuous prudent demand
State under 1st price distribution:
Prudent demand increases before event happen
Convergence under 1st price distribution:
Calculation time: 2s.
State before 10th with all distributions:
skewness aversion

## Slide 25
Case Study
24| Case Study
24 stages
The event happens at the 10th stage
6 skewed price distributions with the same expectation and different variance (skewness)
Sensitivity of model parameters
Discount factors from 0.1 to 1 - A
State cost function parameters - \alpha
State under 2nd price distribution:
Lower discount weaken the prudent influence
Precautionary saving behavior persists greater potential loss from uncertainty at the event time for the same state value, inducing stronger precautionary saving behavior. But, with a saturation effect. The cost of precautionary saving begins to outweigh the cost of expected risk at the event time.

## Slide 26
Case Study
24| Case Study
NYISO DA and RT price
Battery doing arbicharge under non-anticipatory price uncertainty
Real-world case study
Superquadratic model with hard constraints
Quadratic model with quadratic penalty
Superquadratic model exhibits greater variability
Quadratic model captures the mean value of RT price uncertainty
Superquadratic formulation provides richer and more responsive decision behavior.
20-21

## Slide 27
Interpretation and Conclusion
26| Question
We show that risk-aware behaviors in demand response originate from superquadratic state-dependent cost functions and price uncertainty with skewed distributions;
We obtain such results through developing a novel theoretical demand response framework that combines non-anticipatory multi-stage decision-making with superquadratic cost functions;
We introduce the concept of prudent demand, which is the first principle for risk-averse behavior despite a risk-neutral objective.
Future price uncertainty affects immediate consumption decisions, and the extent of this response scales proportionally with the skewness of the price distribution
Conclusion

## Slide 28
Interpretation and Conclusion
26| Question
Practitioners and policymakers should adopt more sophisticated demand models, either through higher-order utility function formulations or the adoption of more accurate risk terms, especially considering physical and behavioral response limitations, thus, capturing real demand behavior and better accounting for demand pattern changes to efficiently design time-varying tariffs
Preparatory savings naturally provide additional backup capacity to the system ahead of emergencies. Thus, operators should not only focus on the event time itself, but also schedule additional generation or implement price incentives in advance to prevent unintended demand peaks.
Discounting factors and the sensitivity of demand to state value changes are important for accurately quantifying prudent behavior.
anticipating and preparing for tail-risk events and controlling the price ceiling exposed to customers, avoiding the direct exposure of retail consumers to highly volatile wholesale market prices.
Practical implication

## Slide 29
Selected Reference
Page 7&8
Jia, L., & Tong, L. (2012, October). Optimal pricing for residential demand response: A stochastic optimization approach. In 2012 50th Annual Allerton Conference on Communication, Control, and Computing (Allerton) (pp. 1879-1884). IEEE.
Morales-España, G., Martínez-Gordón, R., & Sijm, J. (2022). Classifying and modelling demand response in power systems. Energy, 242, 122544.
Deng, R., Yang, Z., Chow, M. Y., & Chen, J. (2015). A survey on demand response in smart grids: Mathematical models and approaches. IEEE Transactions on Industrial Informatics, 11(3), 570-582.
Li, N., Chen, L., & Low, S. H. (2011, July). Optimal demand response based on utility maximization in power networks. In 2011 IEEE power and energy society general meeting (pp. 1-8). IEEE.
Roald, L. A., Pozo, D., Papavasiliou, A., Molzahn, D. K., Kazempour, J., & Conejo, A. (2023). Power systems optimization under uncertainty: A review of methods and applications. Electric Power Systems Research, 214, 108725.
Page 2&9
Kimball, M. S. (1989). Precautionary Saving in the Small and in the Large.
Li, L., & Peter, R. (2021). Should we do more when we know less? The effect of technology risk on optimal effort. Journal of Risk and Insurance, 88(3), 695-725.
Ebert, S., & Wiesen, D. (2011). Testing for prudence and skewness seeking. Management Science, 57(7), 1334-1349
Peter, R. (2017). Optimal self-protection in two periods: On the role of endogenous saving. Journal of Economic Behavior & Organization, 137, 19-36.
Page 11
Shapiro, A., Dentcheva, D., & Ruszczynski, A. (2021). Lectures on stochastic programming: modeling and theory. Society for Industrial and Applied Mathematics
Others
Boyd, S. P., & Vandenberghe, L. (2004). Convex optimization. Cambridge university press
Zheng, N., Jaworski, J., & Xu, B. (2022). Arbitraging variable efficiency energy storage using analytical stochastic dynamic programming. IEEE Transactions on Power Systems, 37(6), 4785-4795
28| Reference

## Slide 30
Thanks!
&
Q&A
For all details, please reference to - https://arxiv.org/abs/2405.16356